## Slide 1: Optics studies for the VHEE experiment at CLEAR
Eugenio Senes, Wilfrid Farabolini
11 September 2018

## Slide 2: Beam dynamics model
226
174
226
174
226
226
224
226
224
226
2870
Defoc.
Quad
355
Foc.
Quad
350
Foc.
Quad
360
Defoc.
Quad
515
Foc.
Quad
510
Foc.
Quad
520
MTV
390
1130
200
300
Movable
phantom and
screen
Magnetic
length
QL3 characteristics | 
Nominal gradient [T/m] | 11.2
Inscribed radius [mm] | 29
Integrated gradient [Tm/m] | 2.53
Nominal current at 11.2 T/m [A] | 200
Temperature rise [oC] | 16
Probably difficult to obtain a final focal length of 250 mm
(reduce energy, increase current beyond 200 A ?)
f = 1 / (k . l)
k [m-2] = 300. g [T/m] / p [MeV]
f = 264 mm at 200 MeV with 200 A
MADx model of the line at https://github.com/esenes/CLEAR-irradiation-water-tank.git

## Slide 3: Angle calculation
√(ε(βentrance-βcentre )
Beam spot size
2√(βcentre * ε)
l

## Slide 4: Problem: beamline aperture
The beta function is parabolic in a drift
A tight squeeze implies high beta peaks before in the line
The aperture is limited to 40 mm diameter, which means at best a 20 mm beam sigma
This limits the angle quite a lot: e.g. to get a 2.95 deg angle on flat beam
~3 deg angle
Would need a 160 mm vacuum chamber at least !

## Slide 5: Partial solution: scraping in one plane
Some solutions are feasible, if one accept to scrap in one plane
Also requires 190% current of the limit on quadrupole 360 …
E.g. 2.5 deg angle:
Beam pipe

## Slide 6: So what can we aim for ?
Let’s get back analytical:
  The beta function is parabolic in a drift
  The angle is calculated as mentioned in slide 2
Beam parameters
  ε = 4 um
  βstart line = 20 m
  αstart line = -0.5

## Slide 7: A feasible case: 1.95 deg in both planes
1.95 degrees angle
Requires overpowering of Q510 (105%) and Q520 (130%)
Same story on the scraping …

## Slide 8: Best feasible case: 2.6 deg in both planes
Requires basically overpowering of just Q520 (130%)
Same story on the scraping …

## Slide 9: The bottom line (IMO):
The angle depends on the beam size at the entrance in the box
A stronger squeeze in the box means losses scraping
  To be checked if the losses are impressing the foils via x-rays
  Scraping = smaller emittance = smaller final angle
  Could make sense in one plane, not in both
It does not look realistic to promise angles greater than 3 degrees.
w.r.t. 200 A nominal current (k1=16.8)
72%
85%
100%
103%
99%
129%

## Slide 10: The bottom line (IMO): (2)
Of course, the stronger we can power the quadrupoles, the bigger angle is obtainable.
  But the bigger we go, the worst it is contain the beta function in at least a plane …
  Eventually one can try to overpower just the last one with a working optics
  Do the quadrupoles saturate if overpowered ? The are not tested at higher currents than nominal 200A
We need an input from the users on which angle is acceptable for them (multiple coulomb scattering in the water…)
Else the last resource is try to move the quadrupoles of the triplet (not simulated)

## Slide 11: Trimming a behaving solution:
Starting from the 2.6 degrees solution
Last quadrupole at 140%  2.96 degrees angle
This is the best result achieved so far, still with big losses in the y plane.

## Slide 12: Spares

## Slide 13: Calculations baseline
MADx model at https://github.com/esenes/CLEAR-irradiation-water-tank.git
Beam parameters at the beginning of MQF350:
  βx = βy = 20 m
  αx = αy = -0.5
  εx = 4 um

## Slide 14
2.6 deg
Last quad 130%