## Slide 1: Optics for the VHEE experiment at CLEAR
Eugenio Senes, Karolina Kokurewicz, Wilfrid Farabolini, Roberto Corsini
13 September 2018

## Slide 2: Beam dynamics model
226
174
226
174
226
226
224
226
224
226
2870
Defoc.
Quad
355
Foc.
Quad
350
Foc.
Quad
360
Defoc.
Quad
515
Foc.
Quad
510
Foc.
Quad
520
MTV
390
1130
200
300
Movable
phantom and
screen
Magnetic
length
QL3 characteristics | 
Nominal gradient [T/m] | 11.2
Inscribed radius [mm] | 29
Integrated gradient [Tm/m] | 2.53
Nominal current at 11.2 T/m [A] | 200
Temperature rise [oC] | 16
Probably difficult to obtain a final focal length of 250 mm
(reduce energy, increase current beyond 200 A ?)
f = 1 / (k . l)
k [m-2] = 300. g [T/m] / p [MeV]
f = 264 mm at 200 MeV with 200 A
MADx model of the line at https://github.com/esenes/CLEAR-irradiation-water-tank.git

## Slide 3: Caveats:
All the optics have been calculated for 4 um geometrical emittance at 200 MeV. So at lower energies the gun has to be retuned to produce a smaller emittance (laser beam spot size ?)
Result to be checked after:
  Optics measurements for the initial parameters
  Quadrupoles overpowering possibilities

## Slide 4: Calibration runs: flat optics
Round beam of ~9-10 mm of diameter constant along the phantom
Magnet | Current @200 MeV [A] | Current @150 MeV [A] | Current @100 MeV [A]
QF350 | 121.4 | 91.1 | 60.7
QD355 | -170.5 | -127.9 | -85.2
QF360 | 200 | 150 | 100
QF510 | 124.6 | 93.5 | 62.3
QD515 | -145.1 | -108.8 | -72.6
QF520 | 147.6 | 110.7 | 73.8

## Slide 5: Constant focus optics:
Focusing angle 5.3 deg
As discussed with Karolina, the focus will be constant to maintain the angle and the phantom will be moved
Please note that the phantom is displaced in reality w.r.t. the plot. The focal point is at ~7cm from the entrance with the present setup
Magnet | Current @200 MeV [A] | Current @150 MeV [A] | Current @100 MeV [A]
QF350 | 118 | 88.5 | 59
QD355 | -169.9 | -127.4 | -84.9
QF360 | 200 | 150 | 100
QF510 | 200 | 150 | 100
QD515 | -185 | -138.8 | -92.5
QF520 | 252.5 | 189.3 | 126.23

## Slide 6: Constant focus optics: overcharging the last quad
QF520 @ 280A
6.2 degrees angle
Focal point 5 cm earlier than present optics
QF520 @ 300A
Focal point 8 cm earlier than present optics