## Slide 1: Beam dynamics model
226
174
226
174
226
226
224
226
224
226
2870
Defoc.
Quad
355
Foc.
Quad
350
Foc.
Quad
360
Defoc.
Quad
515
Foc.
Quad
510
Foc.
Quad
520
MTV
390
1130
200
300
Movable
phantom and
screen
Magnetic
length
QL3 characteristics | 
Nominal gradient [T/m] | 11.2
Inscribed radius [mm] | 29
Integrated gradient [Tm/m] | 2.53
Nominal current at 11.2 T/m [A] | 200
Temperature rise [oC] | 16
Probably difficult to obtain a final focal length of 250 mm
(reduce energy, increase current beyond 200 A ?)
f = 1 / (k . l)
k [m-2] = 300. g [T/m] / p [MeV]
f = 264 mm at 200 MeV with 200 A

## Slide 2: Open beam dynamics points
Working MADx model at https://github.com/esenes/CLEAR-irradiation-water-tank.git
Open points:
  What is the acceptance of the line (in mm) ? A tight squeeze means high beta peaks before
  The quadrupoles are rated for 200A. Is a current overhead really feasible or is this a strict limit ?
  Can we eventually think to move some quadrupoles on the line ? Or is it too much work ?
  What are realistic beam parameters ? I assumed at the beginning of MQF350:
    βx = βy = 10 m
    αx = αy = -0.5
    εx = 10 um Are these reasonable values ? (values in the logbook can differ quite a lot)
Water tank
β_x

## Slide 3: Open beam dynamics points
More input from the user side:
  Is the irradiation symmetry so important ? If we focus, say, 20 cm after the entrance instead of 15 cm is it a problem ? This would relax the strength of the last quad a bit …
  Round beam is necessary or a flat beam is also accepted (we can do both as we have 6 knobs anyway)
  Is the spot size important ? To wich extent (in mm)? Asking a tiny spot reduces the angle possibilities quite a lot
Sqrt(ε(βentrance-βcentre )
Beam spot size
Sqrt(βcentre * ε)