## Slide 1: Optics studies for the VHEE experiment at CLEAR
Eugenio Senes, Wilfrid Farabolini, Roberto Corsini
13 September 2018

## Slide 2: Beam dynamics model
226
174
226
174
226
226
224
226
224
226
2870
Defoc.
Quad
355
Foc.
Quad
350
Foc.
Quad
360
Defoc.
Quad
515
Foc.
Quad
510
Foc.
Quad
520
MTV
390
1130
200
300
Movable
phantom and
screen
Magnetic
length
QL3 characteristics | 
Nominal gradient [T/m] | 11.2
Inscribed radius [mm] | 29
Integrated gradient [Tm/m] | 2.53
Nominal current at 11.2 T/m [A] | 200
Temperature rise [oC] | 16
Probably difficult to obtain a final focal length of 250 mm
(reduce energy, increase current beyond 200 A ?)
f = 1 / (k . l)
k [m-2] = 300. g [T/m] / p [MeV]
f = 264 mm at 200 MeV with 200 A
MADx model of the line at https://github.com/esenes/CLEAR-irradiation-water-tank.git

## Slide 3: Convergent case: 5.1 deg beam cone aperture
Convergent beam in the x-plane, slightly divergent on the y-plane.
Result to be checked after:
  Optics measurements for the initial parameters
  Quadrupoles overpowering possibilities
Magnet | k1 | Current set on 200A
QF350 | 12.33 | 74%
QD355 | -15.43 | 92%
QF360 | 16.90 | 101%
QF510 | 15.89 | 95%
QD515 | -15.68 | 93%
QF520 | 21.87 | 130%

## Slide 4: Flat optics:
Not particularly challenging
Implemented with overpowering of the last quadrupole like the former solution
Magnet | k1 | Current set on 200A
QF350 | 15.28 | 90%
QD355 | -15.13 | 90%
QF360 | 13.29 | 79%
QF510 | 13.80 | 82%
QD515 | -14.73 | 88%
QF520 | 21.57 | 128%

## Slide 5: Flat optics for calibration:
Same as before
4.72 mm beam spot
No overpowering required
Magnet | k1 | Current set on 200A
QF350 | 10.2 | 61%
QD355 | -14.32 | 85%
QF360 | 16.8 | 100%
QF510 | 10.47 | 62%
QD515 | -12.19 | 72%
QF520 | 12.40 | 73%